## Slide 1
CONTINUOUS WAVE MODULATION
Dr.Y.Mallikarjuna Rao M.Tech., Ph.D
Professor & Head of ECE
Santhiram Engineering College
hod.ece@srecnandyal.edu.in

## Slide 2
Syllabus
1.INTRODUCTION
  1.1 THE COMMUNICATION PROCESS
  1.2 COMMUNICATION CHANNELS
  1.3 BASE BAND AND PASS BAND SIGNALS
  1.4 ANALOG VS DIGITAL COMMUNICATIONS
  1.5 NEED FOR THE MODULATION
2. AMPLITUDE MODULATION
  2.1 AM AND ITS MODIFICATIONS-DSB;SSB;VSB
  2.2 FREQUENCY TRANSALTION
  2.3 FREQUENCY DIVISION MULTIPLEXING
3. ANGLE MODULATION
  3.1. FREQUENCY MODULATION
  3.2. PHASE MODULATION
  3.3.PHASE LOCKED LOOP
  3.4 NON LINEAR EFFECTS IN FM
  3.5 SUPERHETRO DYNE RECEIVERS
Continuous Wave Modulation Dr.Y.Mallikarjuna Rao 08-04-2022 01/34

## Slide 3
What is Modulation?
MODULATION :A process by which some characteristic of a carrier is varied in accordance with a modulating signal
SINUSOIDAL CONTINUOUS –WAVE (CW)MODULATION
Amplitude modulation
Angle modulation
From fig
(a) sinusoidal carrier
(b)base band signal or message signal
(c) Amplitude modulation
(d) Frequency modulation
Continuous Wave Modulation Dr.Y.Mallikarjuna Rao 08-04-2022 02/34

## Slide 4
1.1THE COMMUNICATION PROCESS
Continuous Wave Modulation Dr.Y.Mallikarjuna Rao 08-04-2022 03/44
FIG: BLOCK DIAGRAM OF COMMUNICATION PROCESS

## Slide 5
THE COMMUNICATION PROCESS:
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 04/44
Communication: The process of exchanging information from one point to another through succession processes
Communication system: Broadcasting (radio ; television); mobile communication; RADAR communication; computer communication are some examples of communication system
Source of information: The source of information are carried out in three forms(PPP) which are I) Production II) Propagation and III) Perception
Transmitter: The transmitter modifies the baseband(message) signal for efficient transmission. The transmitter may consist of one or more subsystems: an A/D converter, an encoder and modulator
Receiver : the information is reproduced at the receiver which is decoded in electrical form
User of Information: This is the final stage at which original signal is received in original form
7. Channel: It is a medium between the transmitter and receiver while transmitting the base band signal
      Physical channel Eg: coaxial cable
      Wireless channel Eg: Mobile communication

## Slide 6
Continuous Wave Modulation Dr.Y.Mallikarjuna Rao 08-04-2022 05/44
1.2 THE COMMUNICATION CHANNELS
The communication channel between modulated and demodulated is located in communication system is discrete in nature and is referred as coding channel
The probability of an error can be evaluated as
)
CHANNEL REPRESENTATION:
LOSSLESS CHANNEL:

## Slide 7
1.2 COMMUNICATION CHANNELS
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 06/34
DETERMINISTIC CHANNEL:
NOISELESS CHANNEL:
BINARY REPRESENTATION CHANNEL:

## Slide 8
1.3 BASE BAND AND BANDPASS SIGNALS
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 07/34
BASE BAND SIGNAL : The information or the input to the communication system can be analog. The electrical equivalent of this original information is known as base band signal. Examples : the computer data
BAND PASS SIGNAL : The modulated signal is called band pass signal which is obtained from the shifting of frequency spectrum. Examples : visible light; ultrasound waves.
FIG: spectrum for base band signal FIG: spectrum for band pass signal
where f1 is an lowest frequency f2 is an highest frequency

## Slide 9
1.4 ANALOG VS DIGITAL COMUNICATION SYSTEM
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 08/34
S.NO | ANALOG COMMUNICATION | DIGITAL COMMUNICATION
1 | Signals are transmitted in every time intervals | Signals are transmitted at discrete time intervals
2 | Amplitude , frequency and phase modulation in the transmitted signal represent in the form of message | Amplitude, frequency and phase in the transmitted signal represent in the form of codes
3 | Coding is not possible | Coding techniques can be used to detect and correct the errors
4 | Bandwidth requirement is lower than digital communication | Band width is required due to high bit rates in the system
5 | Not suitable for transmitting signals in military applications | Suitable for transmitting signals in military applications due to coding techniques
6 | FDM is used for multiplexing | TDM is used for multiplexing
7 | Analog modulation systems are PM,AM,FM,PWM,PAM | Digital modulation systems are PCM,DM,DPCM,ADM
8 | Noise immunity is less in AM but improved in FM and PM | Noise immunity is excellent

## Slide 10
1.5 NEED FOR MODULATION
To avoid the mixing of signals
To decrease the length of transmitting and receiving antenna ()
To allow the multiplexing of signals
To remove the interference
To improve the equality of reception i.e. increasing the value of S/N ratio
To increase the range of communication.
Continuous Wave Modulation Dr.Y.Mallikarjuna Rao 08-04-2022 09/44

## Slide 11
2. AMPLITUDE MODULATION
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 10/34
The process in which the amplitude of the carrier wave c(t) is varied linearly with the message signal m(t) keeping other parameters constant is called Amplitude modulation
TIME DOMAIN DESCRIPTION:
Where
Two cases arise depending on compared to unity
CASE 1:
CASE 2:

## Slide 12
2.AMPLITUDE MODULATION
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 11/34
FREQUENCY DOMAIN DESCRIPTION:
[)]+
)
𝛚

## Slide 13
Amplitude modulation
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 12/34
POWER RELATIONS IN AM
In practice, the AM wave is a voltage or current wave.
An AM wave consists of carrier and two sidebands. Hence the AM wave will contain more power than the power-contained by an un modulated carrier.
The amplitudes of the two sidebands are dependent on the modulation index “m”. Hence the power contained in the sidebands depends on the value of m. Hence the total power in an AM wave is a function of the value of modulation index m.
TOTAL POWER IN AM (Pt):
Where E, EUSB and ELSB are the RMS values of the carrier and sideband amplitudes and R is the characteristic resistance of antenna in which the total power is dissipated
CARRIER POWER ():

## Slide 14
Amplitude Modulation
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 13/34
POWER IN SIDE BANDS:
The power in the two sidebands is given as
As we know the peak amplitude of each sideband is

## Slide 15
Amplitude modulation
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 14/44
TOTAL POWER
The total power is given by
---------a
MODULATION INDEX IN TERMS OF Pt AND Pc
From above equ a we can write

## Slide 16
Amplitude modulation
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 15/34
TRANSMISSION EFFICIENCY:
The percentage transmission efficiency is given by
AM POWER IN TERMS OF CURRENT:

## Slide 17
2.1.1Amplitude modulation-SSB
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 16/34
FIG: spectrum for SSB modulation
For the generation of SSB modulated signal to be possible the message spectrum must have an energy gap centred at the origin

## Slide 18
2.1.2 AMPLITUDE MODULATION -DSB
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 17/34

## Slide 19
2.1.2 coherent detection for DSB
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 18/34
)
) )
)
If ф is not equal to either , the output of coherent detector for DSB is simply attenuated by a factor which is independent of time

## Slide 20
DSB
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 19/34
From below fig
)]
FIG: Spectrum for DSB modulation

## Slide 21
Amplitude modulation-VSB
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 20/34
for

## Slide 22
2.2 FRQUENCY TRANSLATION
Continuous Wave Modulation Dr.Y.Mallikarjuna Rao 08-04-2022 21/34
The basic operation involved in single side band modulation is in fact a form of frequency translation, sometimes single side band is referred as frequency changing, mixer and heterodyning
carrier frequency is translated upward carrier frequency is translated downward
It is an important note that mixing is an linear operation.
FIG: BLOCK DIAGRAM OF MIXER

## Slide 23
2.3 FREQUENCY DIVISION MULTIPLEXING (FDM)
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 22/34
MULTIPLEXING: combining independent signals into composite signal suitable for transmission.
FDM: The technique of separating the signals in frequency is referred as FDM

## Slide 24
3.ANGLE MODULATION
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 23/34
In angle modulation the frequency or phase of the carrier signal is varied according to the message signal, but amplitude of the signal is not varied.
          Angle modulation
          Frequency modulation phase modulation
          Frequency of the carrier is Phase angle of the carrier is
          varied according with the varied according with the
          message signal message signal
          is the peak carrier amplitude,
          is carrier frequency and
          is the instantaneous phase deviation.

## Slide 25
3.1 FREQUENCY MODULATION
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 24/34
It is an modulation in which the instantaneous frequency fi(t) is varied in linear proportion with the instantaneous magnitude of the message signal m(t)
Where
carrier frequency =un-modulated carrier frequency
frequency sensitivity
The expression for ɵ(t) for FM is given as
for FM in time domain FIG:FM MODULATED SIGNAL
for FM wave
---modulated carrier wave
Ac------Constant amplitude

## Slide 26
3.1.1 PHASE MODULATION
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 25/34
Phase modulation is the type of an angle modulation in which the angular argument θ(t) is changed in linear proportion with the instantaneous magnitude of the message signal x(t)
Kpm(t)----phase sensitivity
2nfct------Angular argument of un modulated carrier
In time domain it is mathematically represented as s(t)=Ac cosɵ(t)
Ac-----constant amplitude
Kpm(t)---varying phase angle

## Slide 27
3.2 PHASE LOCKED LOOP (PLL)
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 26/34
It is a negative feed back system which Is closely linked to frequency modulation.
It can be used for synchronization.
The frequency of the VCO is precisely set at the un modulated carrier frequency fc
The VCO output has 90°phase shift w.r.t the un modulated carrier wave
Suppose input signal is applied to an PLL is an FM signal defined as
FIG: PHASE LOCKED LOOP

## Slide 28
3.2 PHASE LOCKED LOOP
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 27/34
The angle ф1(t)is related to m(t)t the integral
ф
The output in the phase locked loop is defined by r(t)
With control voltage v(t) applied to the VCO input the angle ф2(t) is related to v(t) by the integral
-------------------------------------------1

## Slide 29
3.2.1 NON LINEAR MODEL OF PLL
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 28/34
FIG: NON LINEARISED MODEL
Phase error is given as v(t)=
From equ’s 1 & 2 we get
= -----------------3

## Slide 30
3.2.2 LINEAR MODEL OF PLL
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 29/34
Equ 3 can be written in frequency form
It isrelated by the fourier transform of PLL as
From above equ
FIG: LINEARISED MODEL

## Slide 31
3.2.1 linear model of pll
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 30/34
            From equ 4& 5 we get
            When we make mod L(f )>>1 then
            In time domain we get

## Slide 32
3.3 NON LINEAR EFFECTS IN FM
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 31/34
)--------6
The FM signal is defined as
Where
From equ 6 we get
From above equ
) +a2
For separating the desired signal of FM wit the carrier frequency fc from that with the carrier frequency 2fc we get
The channel output is reduced by using band pass filter as
)

## Slide 33
3.4 SUPER HETERO DYNE RECEIVER
Continuous wave modulation Dr.Y.Mallikarjuna Rao 08-04-2022 32/34
      FIG:BASIC ELEMENTS OF SUPER HETERO DYNE RECIVER
The super heterodyne receiver as it is often referred to , is a special type of receiver that fulfils all three functions which are
Carrier frequency
filtering
Amplification

## Slide 34
End of Presentation
Continuous wave modulation Dr.Y.Mallikarjuna Rao 07-04-2022 34/34
Thank you all