## Slide 1
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS (MIMO)
Dr.Y.Mallikarjuna Rao M.Tech., Ph.D
Professor & Head of ECE
Santhiram Engineering College
hod.ece@srecnandyal.edu.in

## Slide 2
Outline of the Presentation(PART-1)
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022
4.1 INTRODUCTION TO MIMO
4.2 MIMO SYSTEM MODEL
4.3 ZERO-FORCING REEIVER
4.4 MIMO MMSE RECEIVER
4.5 INTROUCTION TO SVD
4.6 SVD BASED OPTIMAL MIMO TRANSMISSION AND CAPACITY
4.7 OSTBs, V-BLAST REEIVER
4.8 MIMO BEAM FORMING

## Slide 3
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 01/58
Figure 1: MIMO system schematic
INTRODUCTION:
Multiple-Input Multiple-Output (MIMO) wireless communications employ multiple antennas at the transmitter and the receiver. A schematic of a MIMO system with multiple antennas is shown in Figure 6.1.
As MIMO systems have multiple antennas, they can be employed to increase the reliability of the signal through diversity combining as described in the previous chapters. This leads to diversity gain and a net decrease in the bit-error rate of the wireless communication system. In addition, a unique aspect of MIMO wireless systems is that they enable a several-fold increase in the data rate of the wireless communication system by transmitting several information streams in parallel.
This is termed spatial multiplexing. This can be thought of as transmitting multiple parallel streams in space through different spatial modes, i.e., multiplexing information streams in the space dimension as illustrated in Figure 6.1.

## Slide 4
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 02/58
MIMO SYSTEM MODEL:
Consider a MIMO wireless system with t transmit antennas and r receive antennas. Such a MIMO system is also termed an r × t system.Let denote the t symbols transmitted from the t transmit antennas in the MIMO system, i.e., denotes the symbol transmitted from the transmit antenna. These transmit symbols can be stacked to form the t-dimensional vector, also termed the transmit vector,
Corresponding to this transmission, let denote the r received symbols across the r receive antennas in the MIMO systems, which can be stacked as the r-dimensional receive symbol vector,

## Slide 5
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 03/58
Figure 2: MIMO system input-output schematic
Let the complex coefficient represent the fading channel coefficient between the receive antenna and the transmit antenna. Thus, there are a net of rt channel coefficients in this wireless scenario corresponding to all possible combinations of the r receive antennas and t transmit antennas. These can be arranged in a matrix form as
where the r × t dimensional matrix 𝑯is termed the MIMO channel matrix. Let the additive noise at the receive antenna i be denoted by, i.e., denote the additive noise at the r receive antennas. Thus, the net MIMO input output system model can be represented in vector form as

## Slide 6
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 04/58
This is succinctly represented using matrix notation as
Observe that the receive symbol , the receive symbol is given as,
For the special case of t = 1, i.e., single transmit antenna and multiple receive antennas, this is termed as Single-Input Multiple-Output (SIMO) system or the receive diversity system as seen earlier. This can be modeled as
Similarly, for the case of one receive antenna, i.e., r = 1 and multiple transmit antennas, it is termed a Multiple-Input Single-Output (MISO) system model or a transmit diversity system. Its system model is given as

## Slide 7
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 05/58
Finally, for r = t = 1, i.e., a single receive and transmit antenna, it reduces to the single-input single-output (SISO) system, modeled as
The covariance matrix of the noise of the noise vector n defined as

## Slide 8
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 06/58
Finally, to denote the transmission and reception across different time instants, one can add the time index k to the MIMO system model to frame the net model as
Thus, the vectors define the receive, transmit, and noise vectors of the MIMO wireless communication system at the time instant k. Notice that above we have assumed the channel matrix H to be constant or, in other words, not dependent on the time instant k, is also termed a slow fading or quasi-static channel matrix, indicating that the channel coefficients are constant over the block of MIMO vectors that are transmitted.
where the delta function δ (k − l) = 1 if k = l and 0 otherwise. This noise process, which is uncorrelated across different antennas and time instants is termed spatio-temporally uncorrelated noise.

## Slide 9
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 07/58
MIMO ZERO-FORCING (ZF) RECEIVER :
The process to recover the transmitted signal vector x from the received vector y at the MIMO receiver. This can be considered as solving the system of linear equations,
where are the t unknowns and there are r equations corresponding to the r observations . Consider a simplistic scenario, where r = t, i.e., the number of receive antennas is equal to the number of transmit antennas. In this case, the matrix H is square. Further, if the matrix H is now invertible, the estimate of the transmit vector x is still given as
However, frequently, one has more receive antennas than transmit antennas, i.e., r > t. In this scenario, the system is given as

## Slide 10
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 08/58
Hence, one can resort to choosing the vector x which minimizes the estimation error
The above error function is also termed the least-squares error function and the resulting estimator is termed the least-squares estimator. To simplify the analysis going forward, we consider real vectors/matrices y,x, H. The case for complex quantities will be dealt later. The above error function can be expanded as
Consider a multidimensional function g (x). The vector derivative of g (x) with respect to x is defined as

## Slide 11
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 09/58
Consider any vector. Let the function 𝒈be defined as
Hence, it can be seen that,. Therefore, it can be readily deduced that in this case
In fact, it can also be seen that since𝒄, we have
Now, consider the last component. This can be differentiated employing the product rule as

## Slide 12
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 10/58
Hence, employing the above results, the derivative for the error function f (x) can be simplified as
At the optimal estimate of the transmit vector where the above error is minimized, we must have the derivative equal to 0. Using this condition,
Finally, for the case of complex vectors/matrices the transpose in the above expression can be replaced by the Hermitian operator to yield
The above decoder for the MIMO wireless system to decode the transmitted symbol vector x from the received symbol vector y is termed the zero-forcing receiver or simply the ZF receiver. Hence, the zero-forcing decoder can be expressed as

## Slide 13
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 11/58
Properties of the Zero-Forcing Receiver Matrix FZF :
Consider the matrix product, which can be simplified as
However, observe that for r > t, the matrix H is rectangular and strictly speaking does NOT have a matrix inverse. Hence, this matrix FZF is termed the pseudo-inverse of H. Observe that it is, however, not the inverse of the matrix H in the usual sense. For instance, if to be the inverse of H, it must also satisfy the property that. However, we have
Thus, in general, FZF is not the inverse of the channel matrix H. However, if r = t and the matrix H is invertible then the pseudo-inverse is actually equal to the inverse. This can be seen as follows

## Slide 14
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 12/58
Principle of Orthogonally Interpretation of ZF Receiver :
Consider once again the system of equations at the receiver for r > t.
Denoting the column we denote the column of the channel matrix H. Then, the system of equations above can be succinctly represented as
Observe that there are t columns of the channel matrix H, which are . Hence, they represent a t-dimensional subspace. However, the vector y can lie anywhere in the r-dimensional space, and is unlikely to lie exclusively in the t-dimensional subspace represented by the columns of the channel, is shown schematically in Figure3 where aproximación error the error is shown for different choices ofseen that the approximation is minimum, when it is orthogonal to the space spanned by the columns of H. This is termed the principle of orthogonality,
Figure 3:Zero-forcing: principle of orthogonality

## Slide 15
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 13/58
Therefore, since e is orthogonal to the subspace spanned by the columns of H, it follows that it is orthogonal to each of the columns of H. Hence, we have
from which it follows naturally that
This can be derived by substituting the expression in the above result as
Thus, the principle of orthogonally can be conveniently employed to deduce the expression for the optimal ZF MIMO decoder while also giving valuable insights into the decoding procedure.

## Slide 16
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 14/58
MIMO MMSE RECEIVER :
In this,we develop the Minimum Mean-Squared Error (MMSE) receiver for the MIMO wireless communication system. The MMSE receiver is based on a Bayesian approach, meaning that the transmit vector x is assumed to be random in nature. Thus, if denotes the estimated symbol vector, the MMSE receiver minimizes the average or mean of the squared error
To illustrate the development of the MMSE receiver, we consider a single-input multiple-output (SIMO) wireless system, i.e., t = 1, and generalize the result to the case of a MIMO system. Hence, consider the SIMO system model given as
where x is now a scalar transmitted symbol. Thus, the basic problem can be interpreted as estimating the symbol x given the vector Let . One can now define a linear estimator of x as

## Slide 17
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 15/58
We now wish to find the best or optimal linear estimator , which minimizes the mean squared error and hence is also termed the Linear Minimum Mean Squared Estimator (LMMSE). This is frequently also referred to simply as the MMSE, although strictly speaking belongs to the specific class of linear estimators. The average mean squared error is defined as
Employing the form in Eq. (4), the resulting equation can be simplified as
Hence, the average MSE as a function of the receive beam former c, denoted by, is given as
Thus, the optimal beam former c which minimizes the average or mean squared error can be obtained by differentiating with respect to c and setting equal to zero as

## Slide 18
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 16/58
Thus, the optimal LMMSE beam forming vector c is given as 𝒄. This is also termed in signal processing as the optimal Wiener filter. The above can be generalized in the case of complex vectors by replacing the transpose by the Hermitian operation. Hence, the MMSE estimate of x is given as
We now compute the MMSE receiver for the MIMO wireless system. Consider again the MIMO system model given as
Let the transmit symbols be such that each is of power, with elements on different transmit antennas being uncorrelated,. Hence, the covariance of the transmit symbols is given as

## Slide 19
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 17/58
Hence,, the covariance of the receive vector y can be simplified as
Further, the cross-covariance matrix can be simplified as
Thus, the optimal MMSE receiver is given as

## Slide 20
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 18/58
Hence, the MMSE estimate of the transmit vector x is given as
We now derive an alternative structure for the MIMO MMSE receiver. Observe that, we have,
Thus, the MIMO MMSE receiver in Eq. (5) can also be expressed as
Thus, if r > t, inversion of the latter matrix is of a lower computation complexity. Since this is frequently the case in MIMO wireless systems, the alternative MIMO MMSE receiver version is more popular for implementation.

## Slide 21
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 19/58
Robustness of MMSE to Noise Amplification :
Consider the SISO case for which H = h. The system model is given as
The MMSE estimate of x is given from Eq. (5) as
Thus, it can be seen that for |h| ≈ 0, the MMSE receiver becomes
Thus, since it does not lead to division by a quantity close to 0, unlike the ZF, it does not lead to noise enhancement

## Slide 22
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 20/58
Low and High SNR Properties of the MMSE Receiver :
Consider the expression for the MMSE receiver in Eq. (6). Observe that at high SNR, i.e.,, the term dominates over. Hence, we have
Employing this approximation in the MMSE receiver in Eq. (6), we have
On the other hand, at low SNR, i.e. , as, the term is negligible compared to . . Thus, we have

## Slide 23
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 21/58
Employing the above approximation at low SNR, the MMSE receiver can be simplified as
which reduces to the matched filter, i.e., proportional to . Thus, the optimal MMSE receiver can be approximated as the zero-forcing receiver at high SNR, while at low SNR, it behaves similar to the matched filter. This behaviour of the MMSE decoder is schematically represented in Figure 4.
Figure 4 : MIMO MMSE receiver: asymptotic behaviour

## Slide 24
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 22/58
INTROUCTION TO SINGULAR VALUE DECOMPOSITION (SVD) :
The singular value decomposition (SVD) of the MIMO channel matrix 𝑯, which is a very important tool to understand the behavior of a MIMO wireless communication system.
Consider an r × t MIMO channel 𝑯 with r ≥ t, i.e., Number of receive antennas greater than or equal to the number of transmit antennas. The SVD of the channel matrix 𝑯 is given as
where the matrices U, Σ, V, which are r × t, t × t and t × t dimensional respectively, satisfy important properties, which we examine next. The columns of the matrix U and V are norm, i.e., we have

## Slide 25
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 23/58
Further, the columns of matrix U and V are orthogonal, i.e.,
Thus, the columns of matrices U and V are orthonormal. As a result, the t × t dimensional square matrix V is unitary, i.e.,
Otherwise, U simply satisfies the relation. Further, the quantities are known as the singular values of the matrix Σ. These singular values are non-negative and ordered, i.e., each and
Finally, an important property of the singular values is that the number of nonzero singular values is equal to the rank of the matrix H.

## Slide 26
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 24/58
SINGULAR VALUE DECOMPOSITION AND MIMO CAPACITY:
The singular value decomposition is central to understanding the spatial multiplexing properties of the MIMO channel and deriving the fundamental limit on the capacity of the MIMO channel. Consider the r × t MIMO wireless system,
Let the SVD of the channel matrix H be given as. Thus, replacing H with its SVD, the above MIMO system model is given as
At the receiver, multiplying by , we have
Further, prior to transmission, let the transmit vector x be generated as, where the vector contains the transmit symbols. This operation is termed as transmit precoding. Thus, substitute this expression for x above, we have

## Slide 27
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 25/58
The above equivalent system model of the MIMO system after the receive and transmit processing operations can be explicitly written as
The above system can, in fact, be written in a much simpler decoupled form as
Thus, the above equivalent system represents the parallelization of the MIMO channel with t information streams being transmitted in parallel. Also, the covariance of the modified noise can be derived as

## Slide 28
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 26/58
Thus, once again, the noise has a covariance proportional to the identity matrix, indicating equal variance, uncorrelated noise components. Further, the variance of each noise component , is equal to. Consider now the parallel MIMO channel above. This is given as
From the above expression for the SNR of the channel, the Shannon capacity of the channel can be derived as
FIGURE 4 MIMO SVD PARALLEL CHANNELS
Thus, the MIMO system can be thought of as a collection of t parallel data pipes, with capacities

## Slide 29
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 27/58
Thus, the net MIMO C capacity is given as the sum of the individual capacities
The total power P at the transmitter can be allocated to the individual streams to maximize the net capacity. Thus, one can maximize the above sum capacity subject to the power constraint
OPTIMAL MIMO CAPACITY:
The optimal MIMO power allocation problem can be formulated as
where s.t. in the above problem statement stands for subject to and denotes the optimization constraint. We employ the standard Lagrange-multiplier-based technique for the above constrained optimization problem.

## Slide 30
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 28/58
Denoting the Lagrange multiplier by λ, the Lagrangian cost for the above optimization problem can be formulated as
where. Differentiating with respect to and setting equal to 0, we obtain
Where the function if and 0 otherwise. This is because of the fact that each power, i.e., power cannot be negative. It now remains to find the Lagrange multiplier λ, which can be found from the constraint equation as

## Slide 31
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 29/58
The above optimal power allocation is also termed water filling. This can be seen as follows. Consider a vessel with t bars and the height of the bar equal to. It water is poured into this vessel to the level 1 λ then the level of water at the bar isis shown in below figure
Figure 5: MIMO water-filling capacity
From above equation ,It can be solved iteratively as follows. Set N = t initially. Assume for 1 ≤ i ≤ N. Solve the equation

## Slide 32
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 30/58
ALAMOUTI CODE (OSTBCs):
The Alamouti code is a space-time code proposed for a 1 × 2 MISO system. The interesting aspect of the Alamouti-code is that it achieves a diversity order of 2 without CSI at the transmitter.
Consider two symbols . In an Alamouti-coded system, in the first transmit instant, the symbol is transmitted from the transmit antenna 1, while is transmitted from the transmit antenna 2. Therefore, the transmit symbol vector in the first time instant is given as
Further, the received symbol at the receiver corresponding to this transmission is given as
In the second time instant, the symbol is transmitted from the first transmit antenna, while is transmitted from the second transmit antenna. Therefore, the transmit symbol vector in the second time instant is given as

## Slide 33
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 31/58
Further, the received symbol can be expressed as
Consider the conjugate of at the receiver, the above equation can be simplified as
Now, the received symbols and from equations (11) and (13) above can be stacked to write the combined system model for the first and second time instants in the Alamouti code as
Thus, both the symbols have been stacked which effectively converts the Alamouti coded system into a 2 × 2 MIMO system, with the channel matrix

## Slide 34
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 32/58
Moreover, observe a very important property of the Alamouti channel matrix. Consider the columns of the channel matrix given as
Then, we have, given as
Consider now beam-forming using the vector defined in terms of as
One can now employ this as a receive beam former to derive the processed symbol as

## Slide 35
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 33/58
Further, since is a unit-norm vector, is Gaussian noise with variance . Therefore, the SNR at the receiver is given as
Similarly, to decode , the beam former is given as
Hence, the net output SNR of each stream is
Hence, the Alamouti code is also termed an Orthogonal SpaceTime Block Code (OSTBC). The term space-time refers to the fact that the Alamouti code involves two symbols which are transmitted over two antennas over two instants of time. Therefore, the symbols are coded across both the space and time dimensions, leading to the name "space-time" code. This is schematically shown in Figure 6.
Figure 6 Alamouti orthogonal space-time block code

## Slide 36
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 34/58
NONLINEAR MIMO RECEIVER V-BLAST :
The first nonlinear MIMO receiver, termed V-BLAST, short for vertical bell labs layered space-time receiver. V-BLAST employs successive interference cancellation (SIC) in which the impact of each estimated symbol is cancelled prior to the detection o f the next symbol. This SIC principle on which V-BLAST is based leads to its nonlinear nature. Consider the MIMO system model given as
Let this matrix be denoted by the t × r matrix Q, i.e.,. Further, let the matrix Q be written as

## Slide 37
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 35/58
Therefore, we have,
The above property can be basically summarized as
From Eq. 16, observe that the system model can be explicitly given in terms of the columns of the channel matrix H as
Employing now the fact thatand, etc., is zero, one can use as a receiver beam-former

## Slide 38
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 36/58
Therefore, performing 𝒚 at the receiver, we have
Thus, can now be employed to decode . Now, the interference caused byis removed from y to form as
In fact, in the last stage, when only one symbol is left for decoding, the effective system model is given as

## Slide 39
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 37/58
MIMO BEAMFORMING :
The context of a MIMO wireless system. Beam-forming basically implies that only spatial dimension is used for transmission amongst the many dimensions that are available. Consider the MIMO system given as
Observe now that the right and left singular vectors respectively, which correspond to the largest singular value , represent the dominant transmit and receive modes of the MIMO system. Hence, one can transmit a single symbol from the transmitter by beam forming along the vector as

## Slide 40
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 38/58
Thus, the symbol is being transmitted along the abstract direction represented by the vector in t dimensional space as shown in Figure 7. Substituting this in the MIMO system model, we have
Therefore, the received signal y can be further simplified as
Figure 6.8 MIMO beam
forming

## Slide 41
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 39/58
One can now perform MRC at the receiver using the beam forming vector as,
Thus, the SNR at the receiver is given as
This MIMO beamforming scheme is termed Maximum Ratio Transmission (MRT). Since only one dimension is being used in this scheme, it results in a simplistic transmission and reception scheme compared to spatial multiplexing MIMO schemes such as MIMO-ZF, MIMO-MMSE, MIMO V-BLAST, etc.

## Slide 42
MULTIPLE INPUT MULTIPLE OUTPUT SYSTEMS
Multiple Input Multiple Output Systems Dr.Y.Mallikarjuna Rao 22-03-2022 40/58
Further, two additional points are worth of being noted about the maximum ration transmission scheme.
Firstly, it is capacity optimal at low SNR.
Secondly, it achieves the full diversity order of MIMO communication, i.e., rt , where r, t denote the number of receive and transmit antennas respectively.

## Slide 43
Outline of the Presentation (PART-2)
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 41/58
4.1 INTRODUCTION TO OFDM
4.2 MULTI CARRIER MODULATION
4.3 IFFT SAMPLING OF OFDM
4.4 OFDM SCHEMATIC
4.5 CYCLIC PREFIX
4.6 OFDM PARALLELIZATION
4.7 OFDM EXAMPLES

## Slide 44
ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 42/58
INTRODUCTION :
Orthogonal Frequency-Division Multiplexing (OFDM) forms the basis for 4G, i.e., Fourth Generation wireless communication systems. OFDM is used in 4G wireless cellular standards such as Long-Term Evolution (LTE) and Wi-MAX (Worldwide Interoperability for Microwave Access).
OFDM is a key broadband wireless technology which supports data rates in excess of 100 Mbps. Similarly, the wireless local area (LAN) standards such as 802.11 a/g/n are based on OFDM.
MOTIVATION AND MULTICARRIER BASICS :
Consider a bandwidth B = 2W available for communication, where W is the one-sided bandwidth, or, in other words, the maximum frequency. For a single carrier communication system, the symbol time T is given as
basically implying that symbols can be transmitted at intervals of seconds each. Therefore, the symbol rate is given as

## Slide 45
ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 43/58
Such a system is termed a single-carrier communication system. In such a system, a single carrier is employed for the entire baseband bandwidth of B. Therefore, roughly speaking, the symbols are transmitted as symbol X(0) from 0 ≤ t < T, symbol X(1) from T ≤ t < 2T, and so on, i.e., roughly one symbol transmitted every seconds.
FIGURE 1 MULTI-CARRIER CONCEPT
Consider now dividing the total bandwidth B into N sub-bands of bandwidth B/N each as shown in Figure 7.1. Each subcarrier can now be represented by a subcarrier. Therefore, the sub-carriers are placed at . . . , . . ., as shown in the figure. For instance, consider the bandwidth B = 256 kHz with N = 64 subcarriers. The bandwidth per sub-band is equal to, which is also the frequency spacing between the subcarriers. We now implement a multi-carrier transmission system as follows.
Consider the subcarrier at the frequency, with

## Slide 46
ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 44/58
Let denote the data transmitted on the subcarrier. Then, the signal corresponding to the subcarrier is given as
The above equation shows the data modulation process over the subcarrier. The N different data symbols are modulated over the N different subcarriers with center frequencies . Hence, there are a total of N data streams. Next we illustrate the scheme for multicarrier transmission.
MULTICARRIER MODULATION :
Consider now the different modulated signals corresponding to the N different subcarriers. These signals are then superposed at the transmitted to form the composite signal s (t) given as
. At the receivers, the individual data streams have then to be isolated from the composite signal s (t) above. This is accomplished as follows. Consider the signal y (t) received as

## Slide 47
ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 45/58
Therefore, to extract , which is the Fourier coefficient corresponding to the frequency , one needs to follow the procedure similar to compute the Fourier series as
In fact, this basically implies that the different sinusoids and are orthogonal. It is this key property of orthogonally which helps extract the different streams modulated over the different subcarriers. This property of orthogonally can be summarized as
The above scheme of transmission on multiple orthogonal subcarriers and the associated data recovery at the receiver is termed Multi-Carrier Modulation (MCM). Also observe that the window of time associated with detection of this multicarrier signal is, which is basically the time period of integration.

## Slide 48
ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 46/58
FIGURE 2: MULTICARRIER MODULATION TRANSMITTER
FIGURE 3 MULTI-CARRIER MODULATION RECEIVER

## Slide 49
ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 47/58
The advantage of an MCM system over the single-carrier system can be understood by considering an example with a transmission bandwidth ofwith which is typically around, i.e.,. Therefore, since the transmission bandwidth, the single-carrier system experiences Frequency-selective fading and inter-symbol interference.
Thus, the most critical and key benefit of this MCM system is that through parallel transmission using multiple narrowband subcarriers, it eliminates the Inter-Symbol interference (ISI), thus avoiding distortion of the received symbols.
IFFT SAMPLING FOR OFDM; OFDM SCHMATIC:
Consider now the composite MCM signal given in Eq. (2). The sample at time instant is given as
This scheme of generating the composite transmit signal through IDFT was proposed by Weinstein and Ebert in 1971. Thus, it drastically reduces the complexity of implementing an OFDM system since it eliminates the need for the bank of modulators corresponding to the different subcarrier frequencies.

## Slide 50
ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 48/58
Observe from the expression above that the sample x (u) is basically the Inverse Discrete Fourier Transform (IDFT) coefficient of the information symbols at the time point. Thus, the Inverse Fast Fourier Transform (IFFT) can be conveniently employed to generate the sample MCM signal.
This technique, where the MCM signal is generated by employing the IFFT operation is termed Orthogonal Frequency Division Multiplexing, or OFDM. At the receiver, to recover the information symbols, one can correspondingly employ an FFT operation. Schematic figures of the OFDM transmitter and receiver with the IFFT and FFT blocks are given in figures 4 and 5 respectively
FIGURE 4: OFDM TRANSMITTER SCHEMATIC WITH IFFT
FIGURE 5: OFDM RECEIVER SCHEMATIC WITH FFT

## Slide 51
ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 49/58
CYCLIC PREFIX :
Consider a frequency-selective channel modeled with channel taps. Thus, the received symbol y at a given time instant n can be expressed as
from which it can be seen that the received symbol at the time instant n experiences inter symbol interference from the previous L − 1 transmitted symbols. Consider now two OFDM symbols as follows.
Let denote the IFFT samples of the modulated symbols while denote the IFFT samples of the previous modulated symbol block Thus, the samples corresponding to these two blocks of OFDM symbols are transmitted sequentially as
Now, consider the received symbol corresponding to the transmission of . This can be expressed a

## Slide 52
ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 50/58
The initial samples of the current OFDM symbol block are being subject to interference from the N − 1 samples of the previous OFDM block. This is shown in Figure 6. Similarly, the received symbol is given as
Let us now consider a modified transmission scheme as follows. To each transmitted OFDM sample stream, we pad the last symbols to make the transmitted stream as follows.
FIGURE 7.6 INTER-OFDM SYMBOL INTERFERENCE

## Slide 53
ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 51/58
Further, this prefix is cyclic in nature, since the same samples from the end of the block are being cycled towards the beginning. Therefore, this is known as the cyclic prefix and is an important aspect of OFDM systems. Consider now the received symbol corresponding to. This is given as
Therefore, the samples are given as
This can, therefore, be expressed as
where ∗N denotes circular convolution of modulo N. Therefore, the output y can be written as

## Slide 54
ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 52/58
Therefore, taking the DFT of at the output, we have
Therefore, the DFT of the samples yields back the original transmitted symbols. The coefficients denotes the DFT of the zero-padded channel filter,
Observe that if a single carrier system was used, and the symbols were transmitted directly then the received symbol would be given as
The set of parallel flat-fading channels can be summarized by the expressions

## Slide 55
ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 53/58
The modified transmitter and receiver schematics with the blocks corresponding to the cyclic prefix are given in figures 8 and 9 respectively. Now, considering the noise at the receiver, the received symbol can be expressed as
FIGURE 7: OFDM PARALLEL SUB-CHANNELS
FIGURE 8: OFDM TRANSMITTER SCHEMATIC WITH CP
where denotes the noise across the subcarrier. A simple detection scheme for is to use the zero-forcing detector for the subcarrier as

## Slide 56
ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 54/58
Further, for a simplistic BPSK or QPSK-modulated transmission, the coherent or matched filter detector can be simply obtained by multiplying with, i.e., the complex conjugate of as
FIGURE 8 : OFDM TRANSMITTER SCHEMATIC WITH CP
Also, one can employ the MMSE detector as
The above equation gives the MMSE receiver across the subcarrier in this OFDM system

## Slide 57
ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 55/58
OFDM BASED PARALLELIZATION :
Consider the transmitted samples x (n) with the cyclic prefix, as given below.
More specifically, the loss in efficiency can be calculated as
However, as the block length N becomes very large, we have
Thus, the loss in throughput approaches 0 as the number of subcarriers N increases, for a fixed length of the delay spread L. Also observe that as the number of subcarriers N increases, the symbol time N B increases as shown in Figure 10.

## Slide 58
ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 56/58
FIGURE 10: INTER OFDM SYMBOL INTERFERENCE WITH INCREASING OFDM SYMBOL TIME
However, as the block length N increases, the decoding delay at the receiver also increases as one has to wait for arrival of the entire block of N samples before it can be demodulated.
Hence, there is a trade-off for increasing N vs. decoding delay. Now, we present another intuitive framework to understand the effect of various parameters. As we have said previously, the duration of the cyclic prefix has to be greater than the delay spread.
Therefore, we need
where denotes the sample time ; denotes the delay spread. Also, the sample time , where B is the total bandwidth of the system and, where is the coherence bandwidth of the system. The above condition implies

## Slide 59
ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 57/58
Combining this with the earlier condition that for efficiency in terms of the effective data rate, we have
This can also be recast as. Interestingly, this is the same condition for frequency flat fading across each subcarrier since this implies that the subcarrier bandwidth is required to be much less than the coherence bandwidth
OFDM EXAMPLE :
we consider a practical Wi-MAX example to illustrate the impact of the various parameters in the design of a complete OFDM system. The total number of subcarriers N = 256, with a bandwidth of 15.625 kHz per subcarrier. Therefore,
Therefore, each subcarrier experiences frequency flat fading. The OFDM symbol time without CP is

## Slide 60
ORTHOGONAL FREQUENCY-DIVISION MULTIPLEXING
Orthogonal Frequency division Multiplexing Dr.Y.Mallikarjuna Rao 22-03-2022 58/58
The raw OFDM symbol time, corresponding to the N = 256 IFFT samples, is 64 μs. Wi-MAX employs a cyclic prefix which is 12.5% of the symbol time. Therefore, the duration of the cyclic prefix is
Thus, the total transmitted OFDM symbol duration with cyclic prefix is. Also, the number of samples in the CP is
FIGURE 11: WIMAX OFDM SYMBOL WITH CYCLIC PREFIX
Thus, the length of the cyclic prefix samples and the total number of samples is 256 + 32 = 288. This break-up of the OFDM symbol in terms of the regular samples and the cyclic prefix is shown in Figure 11. Finally, the loss in spectral efficiency is
This is the loss in spectral efficiency arising because of the addition of the cyclic prefix